## Slide 1: Management of Respirable Crystalline Silica (RCS) in Construction

## Slide 2: Management of RCs in construction

## Slide 3: how much do you know about rcs?
What is RCS?
  Crystalline silica is a naturally occurring substance typically found in stone (particularly sandstone, shale, granite and slate), in sand and also in products such as bricks, tiles, concrete and cement. Respirable Crystalline Silica (RCS) occurs when these materials are worked on to release a very fine, inhalable dust.
How can a person be exposed to RCS?
  Where concrete, stone or sand based materials are altered (during formation, cutting, drilling, polishing or demolition) and made airborne, there is a potential for exposure to crystalline silica dust.
What are the routes of entry for RCS into the body?
  Inhalation is the primary route of exposure to crystalline silica dust.
  When any dust is inhaled, its point of deposition within the respiratory system is very much dependent upon the range of particle sizes present in the dust. The respirable fraction (smallest particle size) of crystalline silica dust can penetrate deep into the lungs.

## Slide 4: how much do you know about rcs?
What are the health impacts of exposure to RCS?
  Silica dust is only harmful when it is inhaled deep into the lungs. Inhalation of fine dust containing crystalline silica can cause silicosis of the lungs, which in severe cases can be disabling, or even fatal.
How can a worker prevent exposure to RCS?
  The respirable fraction of the dust is invisibly fine. Elimination and substitution of RCS containing materials, dust extraction and/or dust suppression are the primary measures advised to control potential exposure.
What Respiratory Protective Equipment (RPE) provides adequate protection?
  Respiratory Protective Equipment (RPE) should either be a FFP3 disposable respirator or a P3 particulate filter fitted to a half or full face mask to provide effective protection and be CE marked. RPE is selected as a control measure when engineering and work practice controls cannot maintain exposures at or below the OELV

## Slide 5: Industry Guidance for RCS
Industry Guidance Manual for Addressing Potential Risks from Worker Exposure to Respirable Crystalline Silica (RCS) on Construction Sites: https://cif.ie/safety/
Approach promoted by industry is to manage all dusts, including but not limited to RCS
Manage dust of differing particle size:
  Floating particles < 75 μm
  Fine-grained dust < 5 μm
  Visible dust > 20 μm

## Slide 6: EU Guidance for Inspectorate
https://osha.europa.eu/en/guidance-national-labour-inspectors-on-addressing-risks-from-worker-exposure-to-respirable-crystalline-silica

## Slide 7: Tools for Training & awareness
Toolbox Talks developed for key work activities that have the potential to generate dust, including RCS.

## Slide 8: Occupational Monitoring for RCS
OELV of 0.1mg/m3 (8 hour reference period), as set down in the HSA’ 2018 Code of Practice for the Chemical Agents Regulations
Support for 2x MSc. students investigating exposure to RCS on construction sites

## Slide 9: Prevalence & duration of dust
Dust remains airborne based on a number of factors, not least particle size (e.g. concrete dust ~1-100 μm; human hair: 100 μm; tobacco smoke ~ 0.1-5 μm).
Assuming a fall height of 1-metre above ground, it would take the following timeframes for dust to settle:
  50 μm - 10 seconds
  10 μm - 5 minutes
  1 μm - 7 hours
  0.1 μm - more than 12 days
Source: Hilti On-Site Dust Solutions 2018

## Slide 10: HSa’ information sheet
https://www.hsa.ie/eng/Publications_and_Forms/Publications/Chemical_and_Hazardous_Substances/Silica_Dust_Information_Sheet.pdf

## Slide 11: Leaner, cleaner, safer work practices
Adopt the Hierarchy of Control Measures: https://www.hsa.ie/eng/Topics/Hazards/
Avoid dry-sweeping;
Select vacuums equipped with HEPA filtration (type-H);
Prioritise dust extraction / containment mechanisms;
Utilise appropriate dust suppression techniques;
Adhere to collective protection measures.

## Slide 12: Leaner, cleaner, safer work practices

## Slide 13: Leaner, cleaner, safer work practices

## Slide 14: THANK YOU, Any questions?